## Slide 1: Wind Turbine
Tamara Roberson
Candidate for Associate Software Engineer

## Slide 2: Who Am I?
Tamara Roberson
Graduating from WSU Everett with a BSEE and CS minor this week
Starting a career in embedded software
Hobby: Board Games

## Slide 3: Who Are You?
Name
Specialization
  Not your job title
  What are you the “go to” person for?
  React? Analog ICs? LaTeX? Regulations?
Hobbies
  Open-Source Software? Video Games? Hiking? Museums?

## Slide 4: The Team
Senior Design Project and Engineering Club Team
US Department of Energy Collegiate Wind Competition
Team of 3 EEs, 1 ME
  Club also includes several Business and Communications students for outreach and wind farm business analysis

## Slide 5: Design Considerations
Collegiate Wind Competition rules
Offshore wind turbine designed to be installed in the Gulf of Mexico
Primary goal: stable, clean 48V dc power
Secondary goals:
  Emergency stop and restart
  Power Arduino controller
  Yaw control to realign turbine into the wind

## Slide 6: Project Management
Wrote user stories
  “As a,” “I want to,” “So that”
  Analyzed requirements
  Created tasks
Post-It note Kanban first
  Moved to Trello

## Slide 7: Project Management
Initial work was based on a broad breakdown of subsystems
  This made it difficult to understand what needed to be done
For the second semester, I named myself as project manager
  Studied Project Management on Udemy

## Slide 8: Project Management

## Slide 9: Subsystems
Power Generation
Load Control
Blade Pitch Control
Yaw Control
Wind Speed Sensor
Software and
Communication
Integration Testing

## Slide 10: Power Generation
Axial-Flux Permanent Magnet Generator (AFPMG)
Price, G., Batzel, T.D., Comanescu, M., & Muller, B.A. (2008). Design and Testing of a Permanent Magnet Axial Flux Wind Power Generator.

## Slide 11: Power Generation
Needed low cogging torque
4 generators in series
Weight balanced over column
Produces high torque, even at low speed

## Slide 12: Power Generation
Two buck converters ensure the produced power remains just under 48V
  48V maximum allowed for safety
One buck converter at 5V for Arduino
Problem: Two buck converters that are in series require 4.5V each
  9V but Ardiuno is 5V

## Slide 13: Load Control
Linear rheostat
  400W, 200Ω
8 bank optically-isolated relay
Emergency stop button
Arduino controller
  Ethernet port

## Slide 14: Blade Pitch Control
Servo motor was imprecise
Stepper motor could be configured
Control system monitors the rate of change in speed

## Slide 15: Blade Pitch Control
Turbine blades rely on the same Bernoulli’s principle as airplane wings
Increasing the angle of attack improves lift, creating torque
But too high and the laminar flow is broken, causing the turbine to stall
“Angle of attack,” The Aviation Online History Museum, Jun. 1, 2015. [Online]. Available: http://www.aviation-history.com/theory/angle_of_attack.htm.

## Slide 16: Yaw Control
Turbine must rotate to face the wind
Active yaw system provides more control
Wind direction sensor triggers continuous servo motor
  7:1 gear reduction

## Slide 17: Wind Speed Sensor
Hot wire anemometers measure the temperature of a fine wire
Tried 12V hot wire
  Too high
Tried cup anemometer
  Where to mount?
Selected 5V hot wire

## Slide 18: Software
Turbine Arduino
Load Control Arduino
Communicate over UART using a modified Ethernet cable
Turbine sends the load controller a command
  Increase, Decrease, Disable, Maximize
Load controller returns status

## Slide 19: Software: Turbine

## Slide 20: Software: Load Controller

## Slide 21: Testing

## Slide 22: Testing
Tension Test: Need 25 lbf (2000 RPM), Breaking Point: 870 lbf

## Slide 23: Results
Kv Rating: 24 RPM / V

## Slide 24: Results

## Slide 25: Acknowledgments
Electrical
Boris Gindlin
Steven Fordham
Mechanical
Dan Gilles
Everett Wind Energy Team
Dr. Gordon Taub
Ryan Phillips
Taylor Funk
Quinn Yackulic
James Garfield
Eric Martin
Zach Epperson
Mariana Nicole Tejada
Yulia Fedorchenko
Kaitlin Jones
Garrett Bassen